## Slide 1: NEXT GENERATION 9-1-1 Tennessee Information for Public Safety
TIPS: 2015 Q1 Update
Presented by OIR-GIS Services

## Slide 2: What it is and how it works
Next Generation 9-1-1

## Slide 3: GIS and NG911
Tennessee Information for Public Safety (TIPS)
  Conforms to National Emergency Number Association (NENA) Standards
    Street Centerlines
    Address Points
    Emergency Service Number (ESN) Polys
  Uniform GIS Platform
    ESRI ArcGIS Based
      Not using Arc at all Districts
      Product provided is ArcGIS Based
    Currently receiving weekly updates
      All 100 Emergency Communications Districts (ECDs)
Notes: TIPS

## Slide 4: Regional Stats
The Stats:
  100 ECDs broken up by region
    94 county ECDs
      Overton and Pickett Co in Middle TN are combined into one district
    6 municipal ECDs
      5 of which are in East TN
      1 in Middle TN
TN ECDs

## Slide 5: Next Gen vs. Current System
Critical parts in current system:
  MSAG (Master Street Address Guide)
  ALI (Automatic Location ID)
    Separately maintained, apart from GIS
    Provided by phone co – record of each phone line
      Tied to addresses
Problems with current system
  Separate records
    Multi step process to update MSAG, ALI and GIS
  Potential for missing addresses/streets in GIS
Solution: Next Generation 9-1-1
  Next Gen employs seamless integration of GIS into 9-1-1
    GIS is Everything
      ECDs’ GIS data will be default “correct” dataset moving forward
      Phone co records (ALI) will be validated against GIS data
    Edit GIS data – Done!

## Slide 6: Emergency Service Numbers
All 100 ECDs have seamless call routing (ESN) boundaries in State GIS database
  Nearly 2,000 ESN polygons within the State of TN
Did You Know?
  TN has no “official” county boundaries
    Each County (and ECD) maintains their own boundary
      None match
    TDOT maps and signs are simply “close approximations”
  OIR GIS orchestrated Herculean task of matching all ESN (Emergency Service Number) boundaries
    Used for call routing only
TN ESNs
Notes: Stress that ESN boundaries are used for call routing only. Taxes, voting, etc. are not affected.

## Slide 7: Public Safety Answering Points
PSAPs polygons are related to ESNs
  Routing information is tied to the PSAPID field within ESNs
    Call plots (Lat/Lon from ALI validated point)
    Lat/Lon falls within a PSAP polygon
    Call routes to that particular PSAP
  For visual reference, ESNs are dissolved here on the PSAPID field
    Some ECDs have multiple PSAPs
TN PSAPs
Notes: Remember that TCS (Seattle) is validating the ALI records against the address points.

## Slide 8: GIS for Next Gen 9-1-1: Update
Near Future
  Statewide database will be replicated between Nashville and Seattle/Phoenix
    Phoenix is backup database
    Testing and vetting happening now
  TCS, based in Seattle, validates the address and street data against ALI records
  Data then sent back to TN for use in NetTN system
    Used for initial call routing
  Jackson area will be first to deploy
    Should be live by sometime late Q1 of 2015

## Slide 9: GIS for Next Gen 9-1-1
Functional relationships
  TN Emergency Communications Board (ECB) contracted with OIR GIS Services to administer the GIS portion of the project
    3 regional technicians were put in place to assist Emergency Communication Districts (ECD’s)
    Standardized TIPS Schema allows easy integration into statewide DB
  Data changes upload from ECDs to OIR
    Change detection program has been installed to detect local changes which are sent weekly to OIR-GIS and loaded into a statewide DB
    Why not replicate all ECDs’ data to OIR?
      Not all ECDs using ArcGIS
Working Database
Comparison Database
Change Files
State SFTP
Statewide Database

## Slide 10: Data Life Cycle
Continued…
  GIS data is sent to TCS and AT&T via Enterprise GIS
    TeleCommunications Systems (TCS) uses GIS data to create ALI database
    AT&T creates MSAG and delivers to NetTN System for use in live call routing
      Location Validation Function
      ESNs are used to route to Public Safety Answering Point (PSAP)

## Slide 11: Next Gen: Data Centers
NetTN:
  Data backups stored in Nashville and Knoxville
    Regional hubs in Memphis, Nashville, Chattanooga, Knoxville, Tri-Cities
      Each has a dedicated high speed connection to at least two other regional hubs
  System Used for initial call routing
    Call routing is not the same as dispatch
    Dispatching is up to each district and separate from 9-1-1
      Most districts take calls and perform dispatching

## Slide 12: The 4-1-1 on 9-1-1 Call Processing
When GIS Based Routing is Deployed

## Slide 13: Land Line: Using GIS
The Lat/Lon data is tied to the address point
If the point is in the GIS data, it will be found and the call sent to the appropriate PSAP
  This is the goal – every point in the GIS data
  Ensures fastest call routing
  What if the point isn’t found?
    We go to the next tier
    Rely on centerline data
  First, let’s look at an “ideal” example:

## Slide 14: Land Line: Address Point
Example:
  Call comes in from 309 Rolling Mill Rd
    Address is in GIS data
    Point is located and mapped
    Call is sent to PSAP
  9-1-1 is Done!
    PSAP handles call from here
    Dispatch, etc. is up to ECD

## Slide 15: Land Line: Without Point
Second line of defense: Geocoding
  Takes minimal additional time
  Example: 50 Jones St
  Address is geocoded halfway down on the right side
    A standardized schema is essential for this to work correctly.
    “Out-of-sequence” and “wrong side” addresses will not geocode correctly – but will likely still locate
  Call is routed to appropriate PSAP
If centerline doesn’t exist, or range doesn’t exist, we go to third line of defense
Notes: Schema refers to addressing schema
I say “will not geocode correctly” to say that they will not locate on the structure because it is out of sequence. But, as long as the centerline includes the range, it will geocode.

## Slide 16: Land Line: Without Point – Worst Case
What happens if the call can’t be geocoded?
  Goes to regional default data center
Hypothetical Example:
  Call comes in from somewhere in Maury County
  Unable to locate point
    Geocode attempt
  Unable to geocode
    Doesn’t plot within an ESN
  Sent to Nashville office
    PSAP answers and transfers
      Time delay!!
        Avoid this scenario!

## Slide 17: Cellular Phone Calls
Handled solely by location
  No address information is involved as in land-line calls
  AT&T bases locations off of cell tower triangulation
  All other carriers use GPS location
    All initialized phones have GPS receiver capability
When call is received:
  Phase 1
    Displays location at “handling tower”
      Happens immediately
  Phase 2
    Refined location based on carrier method
    Takes a few seconds for Phase 2 to come to PSAP
      Maximum time delay dictated by FCC

## Slide 18: QUALITY STANDARDS
Standards and QC Metrics

## Slide 19: Feature Classes
Address Points and Centerlines
  Maintained by ECDs
  Updated via weekly upload to State
    Conglomerated into single statewide DB
ESNs
  Changes directed by ECDs via interactive website
    Updated as needed
  Edits maintained by State
    Not all districts have ability to maintain topology
    Calls will be routed based on poly
      Essential that no gaps/overlaps are present

## Slide 20: Quality Control Process
Primary automatic quality checks:
  Data is checked and filtered prior to upload to State
    Done via a new version of Change Detect Script (v2.0)
      Several “pass/fail” fields
      Other fields lumped together and checked for >2% error rate
    If any of these parameters fail, the upload is stopped
      Ensures that we maintain “clean” data in our statewide DB
    Reports are generated, showing any errors that need to be addressed
      ECDs are using these to improve the overall quality of their local GIS data
  Point/poly analysis to ensure address point ESN value matches the ESN polygon where it resides
    Reports of these errors are also generated for ECD benefit
Other manual periodic quality checks:
  Topology
  Compare ALI (Automatic Location ID) table to address points

## Slide 21: Data Quality Status
As of 12/15/2014: All 100 ECDs have data quality at 98% or higher

## Slide 22
Questions?
Manager: Andrew Griswold (615)532-7830
West: Ryan Pittenger (731)421-6819
Middle: Michael Riter (615)770-1102
East: Kevin Williams (865)594-9424
Methaneous